## Slide 1: Summer 2016
IOT Project Log

## Slide 2: 6/10/2016
Progress
  Make sure sensors work
  Run sample codes that use a temperature sensor and a button, and LED display
Next step
  Show data from sensors from browsers
  Understanding for socket.io
  Try to use other sensors

## Slide 3: Notes from experiments
Displaying colorful LED require less voltage(3.3 V)
Displaying String require more voltage(5V)

## Slide 4: Kind of Sensors-I2C-
I2C sensors
  I2C sensors are embedded a tip(processor)
  Communicate with Edison(Arduino) via the processor
  Has clock
  Returns 1 or 0 (Boolean) according to clock
  Use all of 4 lines
I2C port
Edison
GND
VCC
SDA
SCL

## Slide 5: Kind of Sensors-Analog-
Analog Sensors
  3 lines are used to sent data
  power suply i.e. VCC or white code  voltage range[0,5]
  Values from sensors are proportional to voltage
Analog port
Edison
GND
VCC
NC
SIG
GND
VCC
A1
A2
Analog
Sensor

## Slide 6: Kinds of Sensors-Digital-
Return value
  If 2.5V or more  1
  If 2.5V or less  0
Only two lines are required to send data
Digital port
Edison
GND
VCC
NC
SIG
GND
VCC
D1
D2
Digital
Sensor